## Slide 1
Wildland Fire Preparedness & Awareness
Conservation Ontario
Notes: Conservation Ontario's annual Conservation Areas Workshop, a three day training conference for CA staff of all stripes.
looking for someone who could speak to us about wildfire preparedness, risk management, and mitigation. With climate change bringing new challenges and as Ontario’s second largest landowners we’d like to become better educated and prepared.

## Slide 2
Ontario Wildland Fire Response Sectors
Haliburton Fire Management Headquarters Response Sector E1
Fire Management Headquarters
Regional Forest Fire Management Center’s
Cochrane
Timmins
Sudbury
North Bay
Haliburton
Fire Attack Base
Haliburton
Hearst
Red Lake
Dryden
Pickle Lake
Geraldton
Thunder Bay
Kenora
Fort Frances
Chapleau
Wawa
Sioux Lookout
Legend:
Fire Response Sector Boundary

## Slide 3: Why should you think about Wildland Fire?
2021 Fire Season saw the most Hectares burnt in a fire season since 1995
1,201 wildfires in Ontario that MNRF actioned
  78% lightning caused / 22% human caused
  1,058 fires with a full suppression objective
  143 fires either monitored, or modified response
793,533 hectares burned
Notes: 2021: 1,201 Fires including PB’s, totaling 793,533ha
2022: 275 Fires including PB’s totaling only 2,560.3ha
2023: 743 Fires including PB’s, totaling 441,473.8 ha

## Slide 4
Wildland Fire Negative Impacts

## Slide 5
Wildland Fire Positive Impacts

## Slide 6: Wildland Fire Controlled Burns
Prescribed Burning in Ontario;
- Ecological - Silvicultural
- Hazard Reduction – ( Mitigation )

## Slide 7
Fire Triangle: elements required for a Wildland Fire flame to develop/sustain:
Fire Environment: elements that affect the Wildland Fire behaviour once it starts:

## Slide 8
Weather and Wildland Fire
Daytime burning restrictions in relation to daily diurnal effects
Restricted Fire Zones

## Slide 9
North
Wind Direction
Forest Fuels and Wildland Fire
Standing Dead Grass: 29m/min FIC 4,
Boreal Mix Wood: 3 - 4m/min FIC 3,
Boreal Spruce: 9m/min* FIC 5,
Red and White Pine: 2m/min FIC 2,
May 11th, 2023: Actual Weather Observations:
Temp: 23.6 - R/H 34% - Wind: 10km/hr. FFMC 92 – DMC 26 – DC 45 - ISI 10.2 – BUI 26 – FWI 16 High.
Notes: Boreal Mixed wood running 25% Conifer.
Standing Dead Grass at 3.5t/ha and 91-100% cured.

## Slide 13
Immediate Zone
Intermediate Zone
Extended Zone

## Slide 14
Notes: Read off Slide.

## Slide 16
Intermediate Zone 1.5m to 10m
The goal in the Intermediate Zone is to reduce a lot of fire supporting fuel,
Elements in this zone are managed so they do not support fire growth and include naturally occurring fire resistant plants and trees.
Trees:
Because coniferous trees are particularly more flammable than deciduous trees, it is important in this area to consider deciduous trees rather than conifer.
If conifers are still preferred for other factors; then prune and space to lessen fire intensity.
Plants:
Because some plants are particularly more flammable than other, it is important in this area to consider deciduous plants rather than conifer plants.
Plants less flammable:
Fire resistant plants are those that do not readily ignite from flame or embers. They do not contribute to wildland fire intensity and include characteristics such as:
Moist, supple leaves
Limited dead woody stems
Water-like sap with little or no odor
Low amount of sap
Trees more flammable:
Coniferous trees (needles) are more flammable and should be considered avoiding when re-planting within 10 meters of a structure
Spruce species
Fir Species
Pine Species
Cedar Species
Trees less flammable:
Deciduous trees (Leafy) are more resistant to wildland fire and include:
Poplar
Birch
Aspen
Maple
Ash
Cherry
Oak
Basswood
Plants more flammable:
Some plants are more flammable and should be considered avoiding when re-planting within 10 meters of a structure. Characteristics include:
Fine, dry papery material within the plant. (Bark)
Volatile waxes, terpenes or oils, sticky sap with odor.
Leaves are aromatic.

## Slide 17
Extended Zone 10m to 30m
The goal in the Extended Zone is not to eliminate fire by removing all fuel,
However, rather to reduce Fire Intensity by removing some flammable fuels.
Coniferous Tree Spacing
Because coniferous trees are particularly more flammable than deciduous trees, it is important to thin conifers 3m apart between the outermost branches, as a rule of thumb. 3 meters between crowns is enough to reduce crown to crown fire growth.
Coniferous Tree Pruning
Because coniferous trees are particularly more flammable than deciduous trees, it is important to prune conifers lower limbs. As a general direction of guidance 2 meters between crown base height and the ground is enough to reduce Surface to crown fire growth.
2m
2m
2m

## Slide 18
Firesmartcanada.ca
Ontario Interactive Fire
Map:
Federal Fire Hazard
Map: